## Slide 1: GE Washing Machine Teardown Report
Jude Elkins, Joshua Orlett, Mike Fallen

## Slide 2: Components
Component List
Water Inlet
Agitator and Drum
Control Board
Sensors
Drain Pump
Drive Motor
Gearbox
Clutch

## Slide 3: Water Inlet
The Inlet valve has two solenoids, one for hot, one for cold
No Temperature Sensor
All water goes straight into the wash tub

## Slide 4: Agitator and Drum
The agitator and drum always rotate at the same time
The entire drum is contained inside a waterproof plastic tub
Mounted with four suspension arms to the main frame of the dishwasher
The Drum inside the watertight tub

## Slide 5: Control Board
The control board is behind the control knobs
Contains all electronics for the washing machine
One very large capacitor that connects to the drive motor
The large capacitor could pose a safety issue as it caries a charge even after being unplugged

## Slide 6: Door latch
Very simple small solenoid that latches the door closed when running

## Slide 7: Sensors
We only found 3 sensors in the dishwasher
Speed sensor to tell the motor speed
A pressure sensor mounted directly to the main control board
A switch that tells the position of the clutch

## Slide 8: Drain Pump
The drain pump sits at the bottom of the Plastic Tub
Much thicker stack than dishwasher drain pump
The Drain pump mounted to the tub

## Slide 9: Drive motor
Drive motor connects via a belt to the gearbox
3 Phase AC motor?
The Drive motor (green) and the gearbox and drum connection (red)

## Slide 10: Gearbox
Connected to the drive motor by a pulley
Planetary gearbox with 3 planets

## Slide 11: Clutch
The clutch is engaged by a rotating disk spun by an AC motor
During normal operation only the agitator spins
When the clutch is engaged both the agitator and the drum spin
The White disk is pushed up by the actuation arm and then forced back down by the spring

## Slide 12: Flow Diagram
Inlet
Water line
Drain
Wash Drum
Drain Pump
Pressure Sensor

## Slide 13: Improvement Ideas
BLDC drive instead of AC
One unit motor and gearbox to drive the drum
Standardized inlet valve across the GE appliance Line
Switch the machine to mainly DC, more energy efficient and quieter