## Slide 1: GE Dishwasher Teardown Report
Jude Elkins, Joshua Orlett, Mike Fallen

## Slide 2: Components

## Slide 3
Component List
Sump
Distribution Cap & Valve Mechanism
Sensors
Circulation Motor
Drain Motor
Inlet valve

## Slide 4: Sump
The sump is the large plastic plate that all other components connect to.
One main (inlet) hole and one outlet.
All water intake to the pumps is handled through the single drain hole.
The top of the sump showing the Drain hole (red) and Outlet (Green)
The Bottom of the sump showing the attachment for the Circulation pump (A) Drain pump (B) and the inlet for the distribution cap (C)
A
B
C

## Slide 5: Distribution Cap and Valve
The Distribution cap has 4 outlet holes that lead to various parts of the dishwasher.
The white valve uses a pen like cam mechanism to rotate the hole to one of the four on the cap.
The Cap has four outlets, two to the bottom spray head, one to the top spray head, and one that sprays toward the silverware.
The cam mechanism on the bottom of the distribution cap and inside of the valve
The four outlets bottom sprayer(A) silverware (B) top sprayer(C)
The spring and magnets in the valve
A
B
C

## Slide 6: Sensors
We found three sensors on the sump.
A turbidity and temperature sensor.
The Pressure sensor.
Magnetic sensor for the position of the distribution valve.
Turbidity Sensor
Pressure Sensor
Magnetic Sensor
Post for Magnetic Sensor

## Slide 7: Circulation Pump
We did not remove the pump as it was sealed into the sump, and we did not want to break it.
The pump takes water in from the main hole in the sump and outputs through the distribution cap.
BLDC motor

## Slide 8: Drain Pump
The drain pump takes water in from the main sump hole and then outputs through the drain hose.
AC Laminated motor with attached PCB
PCB Controller
Pump with impeller attached
Impeller
Motor with impeller removed

## Slide 9: Flow Diagram
Inlet
Water line
Drain
Sump
Distribution Cap
Bottom Spray head
Top Spray head
Silverware Spray
Position sensor
Pressure sensor
NOTE: The distribution cap can only output to one of the three at a time
Circ Pump
Drain Pump
Turbidity sensor

## Slide 10: Improvement Ideas
Improvement of the distribution cap mechanism
Eliminates drain pump
Will have to index between options but potential for multiple at once
Diverter valve on the circulation pump
Eliminates drain pump
Can toggle between or do both at once

## Slide 11: Flow Diagram (Improved Distro Cap)
Inlet
Water line
Drain
Sump
Distribution Cap
Bottom Spray head
Top Spray head
Silverware Spray
Position sensor
Pressure sensor
Circ Pump
Turbidity sensor

## Slide 12: Flow Diagram (Added Diverter Valve)
Inlet
Water line
Drain
Sump
Distribution Cap
Bottom Spray head
Top Spray head
Silverware Spray
Position sensor
Pressure sensor
NOTE: The distribution cap can only output to one of the three at a time
Circ Pump
Turbidity sensor
Diverter Valve